## Slide 1: Spatial Filtering
Muhammad Umar
Graduate Research Assistant, Ulsan Industrial AI Lab
Department of Electrical, Electronic and Computer Engineering, University of Ulsan
28 September 2026
34
42
71
115
169
163
178
39
34
41
55
88
142
174
33
29
32
51
71
102
150
26
25
29
38
68
76
132
29
30
34
33
53
57
89
28
26
28
31
35
46
62
26
27
29
26
28
29
40

## Slide 2
My academic background
Bachelor of Science
(2019-2023)
Doctor of Philosophy
(2023-Present)
Major: Computer Systems Engineering
Major: AI and Computer Engineering
Research Publications: 25
Journal | Conference
15 First Author: 5 Co-author: 10 | 10 First Author: 3 Co-author: 7
Number of Citations: 395+
Laboratory: Ulsan Industrial Artificial Intelligence Laboratory
Final Year Project
Deepfake Video Detection Using Deep Learning
University of Engineering
and Technology, Peshawar
University of Ulsan,
South Korea
Research Area
Intelligent Fault Diagnosis and Predictive
Maintenance for Industrial Rotating Machines

## Slide 3
Would you trust a diagnosis from the image on the left?
3/33
NOISY INPUT
FILTERED
Same retina. Same data. Different visibility.

## Slide 4
Which image would you trust?
Synthetic salt-and-pepper noise
Original / after ONE line of code
4/33

## Slide 5
Why do we filter images?
BEFORE
AFTER
Medical Imaging
Reduce imaging noise before clinical analysis
BEFORE
AFTER
Security Cameras
Remove night-time grain from CCTV
BEFORE
AFTER
Astronomy
Improve the visibility of faint stars
BEFORE
AFTER
Industrial Inspection
Clean item images before counting or measuring
BEFORE
AFTER
Documents and OCR
Erase scan specks before text recognition
BEFORE
AFTER
Smartphone Cameras
The 'sharpness' in every photo we take
5/33

## Slide 6
Today’s agenda
1
Image basics
›
2
Spatial filtering
›
3
Smoothing
›
4
Sharpening
›
5
Case studies
6/33

## Slide 7
A picture is a grid of numbers
➜ Zoom into any photo and we will find tiny squares called pixels.
➜ Each pixel stores one number:
0
128
255
Black grey white
7/33

## Slide 8
Spatial filtering
➜ Changing each pixel by looking at the pixel and its neighbours.
N
N
N
N
P
N
N
N
N
P = the pixel we are changing
N = its 8 neighbours
Amber box = 3 × 3 neighbourhood
8/33

## Slide 9
How it works: a small window slides over the image
12
15
18
20
22
24
14
30
34
36
25
23
16
32
40
38
27
21
18
33
37
35
29
20
20
22
24
26
30
19
21
23
22
25
27
18
Step A: top-left
12
15
18
20
22
24
14
30
34
36
25
23
16
32
40
38
27
21
18
33
37
35
29
20
20
22
24
26
30
19
21
23
22
25
27
18
Step B: move one to the right
12
15
18
20
22
24
14
30
34
36
25
23
16
32
40
38
27
21
18
33
37
35
29
20
20
22
24
26
30
19
21
23
22
25
27
18
…then the next row
1
Place
the window on a pixel
2
Combine
the 9 numbers with a rule
3
Write
the answer in the new image
4
Slide
to the next pixel and repeat
The main difference between filters is how Step 2 combines the neighborhood values.
9/33

## Slide 10
The math of linear spatial filtering
the new pixel value we are computing
an old pixel inside the 3 × 3 window
the weight: how much that pixel counts
add up all 9 products (s and t go −1, 0, +1)
the kernel (mask): 9 weights
Multiply each neighbor by its weight, then add everything.
10/33

## Slide 11
Smoothing
➜ Reducing unwanted local intensity variations.
➜ Also called blurring or low-pass filtering.
2 smoothing tools:
Averaging filter
Median filter
noisy
smoothed (3 × 3 average)
11/33

## Slide 12
Averaging filter: the math
➜ Each output pixel is the mean of the nine values in a 3×3 neighborhood.
= ×
3×3 averaging kernel
Every weight equals 1/9, and all weights sum to 1.
1
1
1
1
1
1
1
1
1
Add the 9-pixel values in the window
Divide by 9
That is the new centre pixel
12/33

## Slide 13
Averaging filter: example
A flat area (value 10) with one noisy pixel (100):
10
10
10
10
100
10
10
10
10
Sum = 10+10+10+10+100+10+10+10+10 = 180
Mean = 180 ÷ 9 =
20
The noise dropped from 100 to 20. Better, but not gone.
Averaging does not remove the bad pixel. It spreads it over the neighbors.
13/33

## Slide 14
Averaging on a real image: the size of the window matters
original
3 × 3: 9 pixels
9 × 9: 81 pixels
21 × 21: 441 pixels
Bigger window → more noise removed → but more blur (loss of details)
Weakness: averaging cannot tell noise from edges, so edges get blurred too.
14/33

## Slide 15
Median filter: example
10
10
10
10
100
10
10
10
10
Step 1: sort the 9 values
10
10
10
10
10
10
10
10
100
Step 2: take the 5th value (the middle of 9)
➜ Sort the neighbourhood from small to large and take the middle value.
Average
20
Median
10
The true value was 10. The median gets it exactly.
15/33

## Slide 16
Sharpening
Sharpening increases local contrast around edges and fine structures, making intensity transitions appear more distinct.
soft
sharpened
16/33

## Slide 17
An edge is a place where brightness changes fast
1st derivative = change
2nd derivative = change of the change
How much does the brightness change from one pixel to the next?
Is the change speeding up or slowing down? It is + at the start of an edge and − at the end.
➜ Sharpening finds the edges and makes them stronger.
17/33

## Slide 18
The Laplacian as a second-derivative filter
0
1
0
1
-4
1
0
1
0
the Laplacian kernel
(named after Pierre-Simon Laplace)
➜ The Laplacian measures local curvature by adding the second derivatives in the horizontal and vertical directions.
18/33

## Slide 19
The 4-neighbour Laplacian kernel
➜ A one-dimensional second derivative uses the weights [1, -2, 1]. Adding the horizontal and vertical responses produces the 2-D Laplacian.
0
0
0
1
-2
1
0
0
0
Horizontal (x):
+
0
1
0
0
-2
0
0
1
0
Vertical (y):
=
0
1
0
1
-4
1
0
1
0
Laplacian
19/33

## Slide 20
Laplacian response in flat regions and at edges
50
50
50
50
50
50
50
50
50
50
50
200
50
50
200
50
50
200
dark side of an edge
50+50+50+200 − 4×50
+150
50
200
200
50
200
200
50
200
200
bright side of an edge
200+200+50+200 − 4×200
−150
For this kernel, uniform regions produce 0. A dark pixel next to brighter pixels produces a positive response. A bright pixel next to darker pixels produces a negative response.
flat area
50+50+50+50 − 4×50
0
20/33

## Slide 21
Case Studies
CASE 01
Salt-and-pepper noise in microscopy
median filter
CASE 02
Gaussian noise in a portrait
Gaussian (weighted average) filter
CASE 03
Low-contrast lunar surface
Laplacian sharpening
CASE 04
Blurry uploads in a photo app
sharpening + blur screening
21/33

## Slide 22
Salt-and-Pepper noise in microscopy
CASE 01
CONTEXT: Histopathology tissue image
NOISE MODEL: Synthetic salt-and-pepper noise added to 10% of the pixels
EFFECT: Noise obscures nuclei and cell boundaries
OBJECTIVE: Remove impulse noise while preserving structural detail
For an 8-bit image: Salt = 255 | Pepper = 0
22/33

## Slide 23
A 5×5 averaging filter
ATTEMPT 1
Average 5 × 5
BEFORE
AFTER
A 5×5 Averaging Filter Reduces Noise but Blurs Detail
23/33

## Slide 24
A 3×3 median filter
ATTEMPT 2
Median: sort the 9 values, take the middle one
BEFORE
AFTER
Chart: Image quality (PSNR, dB, higher = better)
| Noisy | Avg 3 | Avg 5 | Med 3 | Med 5
PSNR | 15.1 | 23.6 | 25 | 34 | 29.8
A 3×3 Median Filter Best Preserves Detail in This Test
24/33

## Slide 25
Gaussian noise in a grayscale image
CONTEXT: Grayscale portrait used to test image denoising
NOISE MODEL: Gaussian noise causes small random changes across the image
EFFECT: Grain obscures facial features and fine edges
OBJECTIVE: Reduce noise while preserving recognizable structures
Gaussian noise introduces small intensity errors across many pixels.
CASE 02
: clean image : noise : observed image
25/33

## Slide 26
A 5×5 gaussian filter
Noisy input
Box filter 5 × 5
Gaussian filter 5 × 5
Box filter 11 × 11: Over-smoothed
Chart: PSNR (dB)
| Noisy | Box 5 | Gauss 5 | Median 5 | Box 11
PSNR | 21.6 | 27.1 | 28.5 | 27.8 | 23.7
Nearby pixels receive larger weights. This 5 × 5 kernel (σ ≈ 1) reduces noise while keeping more detail than equal-weight averaging.
1/256 ×
1
4
6
4
1
4
16
24
16
4
6
24
36
24
6
4
16
24
16
4
1
4
6
4
1
26/33

## Slide 27
Laplacian sharpening for lunar surface detail
CONTEXT: Low-contrast lunar surface image
IMAGE CONDITION: Small intensity differences make fine structures difficult to see
EFFECT: Crater rims and ridges have weak edge contrast
OBJECTIVE: Enhance fine detail while limiting noise amplification
Sharpening emphasizes rapid spatial changes in intensity.
CASE 03
27/33

## Slide 28
Laplacian sharpening
Original Image
Laplacian Magnitude
Sharpened Image
28/33

## Slide 29
How the Laplacian responds to a blurred edge
Chart: One row of pixels across an edge
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Intensity | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 60 | 110 | 170 | 210 | 220 | 220 | 220 | 220 | 220 | 220
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
1st derivative (slope) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 30 | 50 | 60 | 40 | 10 | 0 | 0 | 0 | 0 | 0
2nd derivative (Laplacian) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 30 | 20 | 10 | -20 | -30 | -10 | 0 | 0 | 0 | 0
Blurred Edge Intensity
First and Second Derivatives
0
1
0
1
-4
1
0
1
0
4-neighbour
1
1
1
1
-8
1
1
1
1
8-neighbour
Sums to 0
Flat areas → 0. It only reacts to change.
Read the two curves:
1st derivative: non-zero along the whole ramp → thick edges
2nd derivative: + at the start, − at the end → thin, crisp detail
The Laplacian uses the 2nd derivative
29/33

## Slide 30
Sharpening and blur detection for a photo app
CONTEXT: Photo-sharing application
IMAGE DEGRADATION: Uploaded photos may contain defocus or motion blur
EFFECT: Blur weakens edges and hides fine texture
OBJECTIVE: Sharpen mildly blurred images and detect severe blur automatically
The application needs enhancement for mild blur and quality screening for severe blur.
CASE 04
30/33

## Slide 31
Automatic Blur Screening
Adjustable Sharpening
How the Laplacian responds to an edge
TASK A
Input,
Detailed mask,
Balanced
The parameter controls sharpening strength. Large values increase edge contrast but can create halos and amplify noise.
TASK B
399
Keep
8
Warn
2
Reject
: uploaded image
: blurred version
: high-frequency detailed mask
: sharpened result
: sharpening strength
Blur score = Var[∇²f]
Sharp photo → many edges → high score
Blurry photo → few edges → low score
Threshold the score: keep, warn or reject
31/33

## Slide 32
The three filters side by side
Averaging filter
1
1
1
1
1
1
1
1
1
Rule
mean of 9 pixels
Best for
Gaussian (grain) noise
Weakness
blurs edges; only dilutes specks
Median filter
mid
Rule
middle of sorted 9 pixels
Best for
salt-and-pepper noise
Weakness
slower (sorting)
Laplacian filter
0
1
0
1
-4
1
0
1
0
Rule
2nd derivative; sharpen f − ∇²f
Best for
making edges crisp
Weakness
boosts noise too
32/33
1/9 ×

## Slide 33
Thank You
For queries, please contact: muhammadumar@mail.ulsan.ac.kr